## Slide 1: Lockout/Tagout and Machine Safeguarding

## Slide 2: Oregon OSHA Public Education Mission:
Consultative Services
Enforcement
Public Education and Conferences
Standards and Technical Resources
We provide knowledge and tools to advance self-sufficiency in workplace safety and health.

## Slide 3: Contact us
Field Offices:
Portland 503-229-5910
Salem 503-378-3274
Eugene 541-686-7562
Medford 541-776-6030
Bend 541-388-6066
Pendleton 541-276-2353
Salem Central:
Toll Free English: 800-922-2689
Toll Free Spanish: 800-843-8086
Website: osha.oregon.gov

## Slide 4: Lockout/Tagout

## Slide 5: Introduction
The key is that the equipment or machines are returned to a ZERO energy state before work begins.

## Slide 6: 3 key elements of an energy control program
Energy control procedures
Employee training
Periodic inspection

## Slide 7: The lockout/tagout rule covers the following employees:
Authorized Employee
The person who services or performs maintenance on machines and equipment.
Affected Employee
The person who operates or uses a machine or piece of equipment which is being serviced.
Other Employee
The person who works in an area where lockout procedures are being used.

## Slide 8: Servicing/Maintenance
Adjusting
Inspection
Modifying
Constructing
Re-tooling
Lubricating
Installing
Setting-up
Removing jams
Cleaning

## Slide 9: Sources of energy capable of causing serious injury
Electrical
Pneumatic
Gravity
Hydraulic
Radiation
Kinetic

## Slide 10: Energy control plan
Intended Use
Procedures to shut down
Lockout/tagout devices
Machinery tests

## Slide 11: Develop a program
List all equipment or machines that need servicing or maintenance;
Identify those machines which could unexpectedly start up or release stored energy while being serviced or maintained;
Determine the steps in the maintenance or servicing task; and
Review each step for the potential of a hazard from all energy sources.

## Slide 12: Lockout/Tagout procedures
Prepare for lockout
Shutdown
Energy isolation
Lockout or tagout application
Controlling stored energy
Verify

## Slide 13: 1) Prepare for lockout
Types and magnitudes of energy
Hazards posed by that energy
Methods to effectively control the energy

## Slide 14: 2) Shut down
Machinery and equipment must be turned off or shut down using the procedures you’ve established for the machine or equipment.

## Slide 15: 3) Energy isolation
All energy isolating devices must be located and operated to completely de-energize and isolate the equipment.

## Slide 16: 4) Lockout or Tagout application
Lockout vs. Tagout
Lockout devices
Tagout devices

## Slide 17: When can an employer use a tagout system?
When an energy isolating device is not capable of being locked out, or
When the employer can demonstrate (prove) that using a tagout system will provide full employee protection.

## Slide 18: 5) Controlling stored energy
Immediately after applying lockout or tagout devices, the authorized employee must ensure all potentially hazardous stored or residual energy is:
relieved
disconnected
restrained

## Slide 19: 6) Verify
Before starting work on a machine or piece of equipment that has been locked or tagged out, the authorized employee must verify that the machine or piece of equipment has been isolated and de-energized.

## Slide 20: Release from lockout or tagout
Equipment
Employees
Removing lockout/tagout devices

## Slide 21: Testing/positioning machines or equipment
Clear the machine or equipment of tools and materials
Remove employees from the machine or equipment area
Remove the lockout or tagout devices
Energize and proceed with testing or positioning
De-energize all systems and reapply energy control measures

## Slide 22: Group lockout/tagout
Primary responsibility
Monitor the exposure status
Coordinate all affected groups
Personal lockout or tagout

## Slide 23: Training
Authorized employees
Affected employees
Other employees

## Slide 24: Training on tagout devices
Tags are warning devices
Tags must not be removed without the authorized employee’s approval
Tags must be understandable
Tags must be able to withstand the environment
Tags may give employees a false sense of security
Tags must be securely attached

## Slide 25: When should employees be retrained?
Whenever there is a change in their job activities
Whenever there is a change in machine, equipment, or process that present a new hazard
Whenever there is a change in your energy control procedures
Whenever there are deviations from or inadequacies in the employee’s knowledge or use of the energy control procedures

## Slide 26: Training documentation
A training certification must contain:
Each employee’s name and date(s) of training
The topics that were covered
Who conducted the training
How the training was done
Pass or fail

## Slide 27: Inspections
An inspection of each energy control procedure must be conducted at least annually.
These inspections must at least include a demonstration of the procedures (steps) and may be implemented through random audits and/or planned visual observations.

## Slide 28: Inspection documentation
The equipment or machine being serviced
The date(s) of inspection
The employees included in the inspection
The authorized employee performing the inspection

## Slide 29: Principles of Machine Safeguarding

## Slide 30: Goals
Describe the basic hazards involving machinery
Introduce control measures

## Slide 31: Purpose
The purpose of machine guarding is to protect against and prevent injury from point of operation, in-running nip points, rotating parts, flying chips, and sparks.

## Slide 32: 3 Basic areas
The point of operation
Power transmission apparatus
Other moving parts

## Slide 33: Hazardous mechanical motions
Rotating
  In-running nip point hazards
Reciprocating
Transverse

## Slide 34: Nip points between rotating elements and parts with longitudinal motions

## Slide 35: Hazardous mechanical actions
Cutting
Shearing
Bending
Punching

## Slide 36: More cutting action examples

## Slide 37: Safeguarding strategies
Guards
Devices
Location and/or distance
Feeding/ejection methods

## Slide 38: Miscellaneous aids
Awareness barriers
Protective shields
Hand-feeding/holding tools
Anti-restart devices

## Slide 39: What makes a guard effective?
Prevent contact
Not a hazard itself
Doesn’t allow objects to fall into moving parts
Safe maintenance
Secure
Conforms with standards

## Slide 40: Guards
Fixed
Interlocked
Adjustable
Self-adjusting

## Slide 41: Fixed
Permanent part of the machine
Not dependent upon moving parts to perform its intended function
Constructed of sheet metal, screen, wire cloth, bars, plastic, or other substantial material
Usually preferable to all other types because of its relative simplicity and permanence

## Slide 42: Interlocked
When opened or removed, the tripping mechanism and/or power automatically shuts off or disengages
Machine cannot cycle or be started until the guard is back in place
Electrical, mechanical, hydraulic, or pneumatic power
Replacing the guard should not automatically restart the machine

## Slide 43: Adjustable
Allow flexibility in accommodating various sizes of stock

## Slide 44: Self - adjusting
Openings are determined by the movement of stock

## Slide 45: Devices
Presence-Sensing Devices
  Photoelectric
  Radiofrequency
  Electromechanical
Pullback
Restraint
Safety trip controls
Two-hand controls
Two-hand trip
Gate

## Slide 46: Some examples of devices
Type A Gate
Presence Sensing
2 Hand Controls

## Slide 47: Location & distance
Walls
Barriers/Fences
Height above worker
Size of stock (single end feed, punching)
Controls (positioned at a safe distance)

## Slide 48: Feeding & ejection
Automatic
Semi-automatic
Robots

## Slide 49: Additional Educational Resources
Oregon OSHA’s YouTube Channel
A-Z Topic Index – Control of hazardous energy
PESO – English to Español

## Slide 50: Thank You!